Configuration of Sterlite SAM300AX

1. Please Note

In this Model Sign Writing of Ethernet /LAN port/LEDs has been wrongly done. Please read LAN4, LAN3, LAN2 & LAN1 as LAN1, LAN2 LAN3 & LAN4 . Therefore various services on different ports will be available /visible as given blow :

| LAN1 | Broadband Internet |
| --- | --- |
| LAN2 | VoIP |
| LAN3 | IPTV |
| LAN4 | Broadband Internet |

2. set your network connection properties IP address 192.168.1.5 and gateway 192.168.1.1 and if pinging is Reply from 192.168.1.1 gateway

Type http://192.168.1.1 on address bar of Internet Explorer.

In User Name type “admin” and password “admin “, click OK.

3. Click Tab Interface Setup then Click Internet, you will find page as given below:

4.Go to “Advance Setup”, then Click on ADSL subTab. Change ADSL Mode to “ADSL2+. “Also change ADSL Type to “Anneure A” and then Save

5. Go to maintenance tab click on SysRestat, select “Current Settings”

And click on Restart Button then popup will open and click on OK.